##### SALEM LEASING

##### OTTAWA 6x4 YARD TRUCK

Make:    Ottawa

Year:      2012 / 2010 EPA Engine

Model:   6x4 DOT/EPA terminal tractor with ABS brake (Highway Legal)

Approximate top speed of 40 miles per hour

Specifications:

Wheelbase: 146"

80,000-lbs yield steel, 3/8” formed mainframe with "L" frame reinforcement

Engine: Cummins ISB 6.7 250HP @ 2300 RPM, 660 lb/ft torque @1600 RPM

2010 Clean Idle Certified

Electronic & charge air cooled with primary fuel filter

Includes lower muffler guard

50 States Certified - “Clean Idle Certified”

Silicone engine and heater coolant hoses with shielded clamps

Fuel water separator with heater (Cummins electronic engine)

Transmission: Allison 3000RDS (6-speed) electronic transmission.

Includes synthetic transmission fluid

Front Axle: Front Axle: Meritor FF-961, 12,000 lbs with 16.5" x 5" brakes

Synthetic oil in front axle with Stemco seals

Leaf spring suspension, 11 leaf left hand, 10 leaf right hand

Rear Axle: Meritor RT40145, 7.17:1 ratio, rated @ 40,000 lbs. with 16.5" x 7" brakes

Front and rear 285mm piloted hubs

Synthetic 75W90 lube in rear axle (tandem rear axle)

Ridewell Dynalastic model 202 tandem axle suspension rated at 48,000-lbs

Lift Height: 17" lift, 5" I.D. hydraulic cylinder 60,000 pound lift rating

Holland FW-35 fifth wheel plate rated at 70,000 pounds

Hydraulic System: Hydraulic system with constant running wet spline PTO and 10 gallon per minute pump with priority steering circuit and a 16 gallon hydraulic tank

Tires: 295/75R22.5 LRG Dunlop SP160 highway tread all around with 22.5x8.25 wheels

Batteries: (3) 12-Volt maintenance free batteries 725cca battery

Electrical: 12-Volt electrical system-negative ground

Raised roof cab with steel side door and aluminum sliding rear door with door locks

Cab fan mounted on a bracket located at the upper right front inside part of the cab

Air conditioner for electronic engines

Heated mirrors, west coast type 16" X 7"

8” Convex mirrors mounted on mirror arms below the standard mirrors

A solid panel in lieu of the standard cab side vent

Vent wing window installed in lieu of the fixed window on the left hand side of the cab

Two additional 5” flood lights mounted rearward on deck

AM/FM radio with CD & auxiliary input for IPOD and MP3 player

Mounted inside cab above windshield

Chassis Paint: “E” coat primer, White PPG-SAC71166A: Powder coat primer frame

with top coat of polyurethane, painted black.

Wheels: Painted "E" coat white

40 gallon round fuel tank mounted on street side

Flexible fenders – Rear

Trailer stops for cab protection

Grease Jockey autolube lube system

TRW steering gear in lieu of Sheppard

Bendix AD-9 air dryer

Standard Features:

Automatic slack adjusters front and rear brakes

Split brake system with bobtail proportioning anti-compounding valves and ABS

Gear box type power steering with mechanical back-up

Electric back-up alarm

Five digit hourmeter

Air ride seat with isolator, vinyl cover and retractable seat belt

Legal width step

55 Degree curbside tapered deck and removable bumper

Three point cab air ride suspension

Electric tilt system for cab

Floodlight mounted roof level, center of cab facing rearward

12 volt-130 amp alternator

ICC Light package

Cab marker lights

7 wire coiled trailer light cable

West coast 16" x 7" mirrors

Speedometer

Reflective markers

Door locks

Horizontal exhaust and vertical stack

Five gallon urea tank

Front and rear tow eyes

See-thru sunvisor

Electric windshield wiper and washer

Mudflaps behind steer and drive axles

Donaldson air cleaner with removable element.

Air cleaner mounted inside engine compartment

Air restriction indicator mounted under the hood

40,000 BTU heater/defroster

Cab side vent (riveted)

Tinted glass all windows.

Wet spline PTO

Cab paint: White PPG-SAC71166A “E” coat primer

Chassis paint: Epoxy primer, top coat polyurethane, painted black

Grab handles, step and platform painted safety yellow

Maximizer fuel reduction system

Price Salem Leasing

Model Year: 2012

Make: Ottawa 6x4 Terminal Tractor (Highway Legal)

Date: 02/02/2012 – Ordered 2/16/2012

Qty:  2

GVW:

P.O. #: 00-385419

Price includes five year Allison warranty

SCIOttawaTA.doc   Quote 12    	DR-49