| SILENCE DIESEL ENGINE DRIVNE WELDER/GENERATOR SERIES 静音*柴油*发电电焊多功能一体机 （CC） | CC/CV |
| --- | --- |
| MODEL型号 |  | EW280DS KH280DS | EW320DS/EW320DST KH320DS | EW400DS/EW400DST KH400DS | EW500DST KH500DS | EW330DS-CC/CV KH330DS | EW390DS-CC/CV KH390DS |
| DC Welder直流焊机 |  |  |  |  |  |  |  |
| Rated Output额定输出 | KW | 8.1 | 9.1 | 12.5 | 18 | 9.8 | 11 |
| Rated Current额定电流 CC/CV | DCA | 260-CC | 280-CC | 380-CC | 500-CC | 300-CC | 340-CC |
|  | DCA |  |  |  |  | 250@100%-CV | 270@100%-CV |
| Rated Voltage额定电压 | DCV | 30.4 | 31.2 | 35.2 | 38 | 34 | 34 |
| Current Range (Single) 电流调节（单把） | DCA | 50-280 | 50-300 | 50-400 | 30-520 | 50-330 | 50-390 |
| Current Range（Dual） 电流调节（双把） | DCA | Null | Null/30-160×2 double operator | Null/30-160×2 double operator | 15-250×2 double operator | Null | Null |
| OCV 空载电压 | DCV | 80 | 80 | 80 | 80 | 80 | 80 |
| Duty Cycle使用率 | % | 50 | 50 | 50 | 50 | 50 | 50 |
| Rated speed额定转速 | rpm | 3,000 or 3,600 | 3,000 or 3,600 | 3,000 or 3,600 | 1,500 or 1,800 | 3600 | 3,600 |
| Type整流形式 | - | Rectified DC output type整流 | Rectified DC output type整流 | Rectified DC output type整流 | Rectified DC output type整流 | Rectified DC output type整流 | Rectified DC output type整流 |
| Applicable Electrode适用焊条 | mm | 2.0-6.0 | 2.0-6.0 | 2.0-6.0 | 2.0-8.0 | 2.0-6.0 | 2.0-6.0 |
| Aux. Power 辅助电源 |  |  |  |  |  |  |  |
| Rated Output额定输出 | KVA | 8 | 10 | 15 | 20 | 6 | 6 |
| Rated Voltage额定电压 | V | 120-220-380-415 | 120-220-380-415 | 120-220-380-415 | 120-220-380-415 | 120-220-380-415 | 120-220-380-415 |
| Phase相数 | - | 3-phase,4 wires三相四线 | 3-phase,4 wires三相四线 | 3phase,4 wires三相四线 | 3-phase,4 wires三相四线 | 3-phase,4 wires三相四线 | 3-phase,4 wires三相四线 |
| Power Factor功率因数 | % | 80 | 80 | 80 | 80 | 80 | 80 |
| Frequency频率 | Hz | 50 or 60 | 50 or 60 | 50 or 60 | 50 or 60 | 50 or 60 | 50 or 60 |
| Rate额定使用率 | - | Continuous 持续 | Continuous持续 | Continuous持续 | Continuous持续 | Continuous持续 | Continuous持续 |
| Excitation 激励方式 | - | Brushless 无刷 | Brushless 无刷 | Brushless无刷 | Brushless无刷 |  |  |
| Driven 耦合方式 | - | Direct Coupling直接耦合 | Direct Coupling直接耦合 | Direct Coupling直接耦合 | Direct Coupling直接耦合 |  |  |
| ENGINE发动机 |  |  |  |  |  |  |
| Model型号 | - | KUBOTA D722 久保田D722 | Kubota D902 久保田D902 (DAIHATSU-KIPOR KM376AG) | Kubota V1305 久保田V1305 | Kubota V3300 久保田V3300 | Kubota D722 久保田D722 | Kubota D902久保田D902 (DAIHATSU-KIPORK M376AG) |
| Type形式 | - | 4-cycle, water-cooled diesel engine四冲程水冷柴油 | 4-cycle, water-cooled diesel engine四冲程水冷柴油 | 4-cycle,water-cooled diesel engine四冲程水冷柴油 | 4-cycle,water-cooled diesel engine四冲程水冷柴油 | 4-cycle, water-cooled diesel engine四冲程水冷柴油 | 4-cycle,water-cooled diesel engine四冲程水冷柴油 |
| Cylinder arrangement缸体 | - | 3-L三缸 | 3-L三缸 | 4-L四缸 | 4-L四缸 | 3-L三缸 | 3-L三缸 |
| Total displacement 排气量 | cc | 719 | 898(1,048) | 1,335 | 3,318 | 719 | 898 |
| Rated Output额定输出 | KW | 13.3 | 14.2/15.3 | 22.1 | 30.6 | 13.3 | 14.2/15.3 |
| Speed转速 | rpm | 3,000/3,600 | 3,000/3,600 | 3,000/3,600 | 1,500/1,800 | 3,600 | 3,600 |
| Fuel燃料 |  | Light diesel oil | Light diesel oil | Light diesel oil | Light diesel oil | Light diesel oil | Light diesel oil |
| Start System启动方式 | - | Electric motor电启动 | Electric motor电启动 | Electric motor 电启动 | Electric motor 电启动 | Electric motor电启动 | Electric motor 电启动 |
| Fuel Tank Capacity燃油容量 | L | 37 | 37 | 37 | 60 | 37 | 37 |
| Battery Capacity电池容量 | - | 12V-36AH | 12V-36AH | 12V-45AH | 12-85AH | 12V-36AH | 12V-36AH |
| Dimension (L×W×H)尺寸 | mm | 1125×688×756 | 1410×710×805 | 1416×710×805 | 2,100×900×1,100 | 1125×688×756 | 1430×760×850 |
| Net Dry Mass净重 | Kg | 385 | 435 | 510 | 1,050 | 397 | 530 |
| Noise level噪音(7m) | dB | 65 | 67 | 67 | 65 | 68 | 68 |
| *KH series for China mainland market with CCC; specifications given herein are subject to change without notice *中国大陆销售产品KH系列通过CCC认证，规格如有变更恕不另行通知 |  |  |  |

| PORTABLE ENGINE DRIVNE WELDER/GENERATOR SERIES 便携式发电电焊一体机 |
| --- |
| MODEL型号 |  | KHD220 | EW240G KH240 | EW240D KH240 | EW320G KH320 | EW320D KH320 | EW120 KH120 |
| DC Welder直流焊机 |  |
| Brush | - | No brush 无刷 | No brush 无刷 | No brush 无刷 | No brush 无刷 | No brush 无刷 | No brush 无刷 |
| Rated Output额定输出 | KW | 5.6 | 6.3 | 6.3 | 9.6 | 9.6 | 3.2 |
| Rated Current额定电流 | DCA | 200 | 220 | 220 | 300 | 300 | 90 |
| Rated Voltage额定电压 | DCV | 28 | 28.8 | 28.8 | 32 | 32 | 32 |
| Open-circuit Voltage 空载电压 | DCV | 70 | 75 | 75 | 75 | 75 | 70 |
| Duty Cycle使用率 | % | 50 | 50 | 50 | 50 | 50 | 60 |
| Rated speed额定转速 | rpm | 3000 | 3600 | 3600 | 3600 | 3600 | 3000 |
| Type整流形式 | - | Rectified DC output type整流 | Rectified DC output type整流 | Rectified DC output type整流 | Rectified DC output type整流 | Rectified DC output type整流 | Rectified DC output type整流 |
| Applicable Electrode适用焊条 | mm | 2.0-5.0 | 2.0-5.0 | 2.0-5.0 | 2.0-6.0 | 2.0-6.0 | 1.6-3.2 |
| Aux. Power 辅助电源 |  |
| Rated Output额定输出 | KW | 2.5 | 3.0 | 3.0 | 3.0 | 3.0 | 3.2 |
| Rated Voltage额定电压 | DCV | 220V-120V | 220V-120V | 220V-120V | 220V-120V | 220V-120V | AC220V |
| Rate额定使用率 | - | 100% | 100% | 100% | 100% | 100% | 100% |
| Driven 耦合方式 | - | Direct coupling 直接耦合 | Direct coupling 直接耦合 | Direct coupling 直接耦合 | Direct coupling 直接耦合 | Direct coupling 直接耦合 |  |
| ENGINE发动机 |  |
| Model型号 | - | Honda GX390/Mitsubishi GT1300/ Kohler CH440 本田GX390/三菱GT1300/ 科勒CH440 | Honda GX390/Mitsubishi GT1300/ Kohler CH440 本田GX390/三菱GT1300/ 科勒CH440 | Diesel KV188FB 柴油KV188FB | Kohler CH640/Honda GX630 科勒CH640/本田GX630 | Diesel KV188FB 柴油KVR2V840 | Kohler CH270 科勒CH270 |
| Type形式 | - | 4-stroke, Gasoline四冲程汽油 | 4-stroke, Gasoline四冲程汽油 | 4-stroke, Gasoline四冲程柴油 | 4-stroke, Gasoline四冲程汽油 | 4-stroke, Gasoline四冲程柴油 | 4-stroke, Gasoline四冲程汽油 |
| Cylinder arrangement缸体 | - | Single cylinder 单缸 | Single cylinder 单缸 | Single cylinder单缸 | Twin cylinder双缸 | Twin cylinder双缸 | Single cylinder 单缸 |
| Total displacement 排气量 | cc | 389/391/440 | 389/391/440 | 456 | 624/688 | 836 | 208 |
| Max Output最大输出 | KW | 9.6/9.6/10.5 | 9.6/9.6/10.5 | 9.6 | 14.7 | 12 | 5 |
| Speed转速 | rpm | 3000 | 3600 | 3600 | 3600 | 3600 | 3000 |
| Cooling System冷却方式 | - | Air cool 空冷 | Air cool 空冷 | Air cool 空冷 | Air cool 空冷 | Air cool 空冷 | Air cool 空冷 |
| Start System启动方式 | - | Recoil (Electric) start手(电)启动 | Recoil (Electric) start手(电)启动 | Electric start电启动 | Electric start电启动 | Electric start电启动 | Recoil start手启动 |
| Fuel Tank Capacity燃油容量 | L | 17 | 6.5 or 17 | 6.5 or 17 | 6.5 or 17 | 6.5 or 17 | 6.5 |
| Battery Capacity电池容量 | - | 12V-26AH | 12V-26AH | 12V-26AH | 12V-26AH | 12V-26AH | ----- |
| Dimension （L×W×H）尺寸 | mm | 750×545×600 | 725×540×570 | 725×540×570 | 930×620×640 | 930×620×640 | 550×460×490 |
| Net Dry Mass净重 | Kg | 105 | 90 | 110 | 155 | 170 | 45kg |
| Noise level噪音(7m) | dB | 73 | 75 | 76 | 75 | 79 | 71 |
| KH series for China mainland market with CCC; specifications given herein are subject to change without notice *中国大陆销售产品KH系列通过CCC认证，规格如有变更恕不另行通知 |  |